## Slide 1: IP Enabled Ride-on
Powered by Cisco IoX
Paul Beyleveld
Consulting Systems Engineer
September 2016

## Slide 2: Cisco IP Enabled Ride-on

## Slide 3: The Tech
Cisco IP Camera
Cisco 6050
Cisco IR829
Custom Electronics

## Slide 4: Demo

## Slide 5: Cisco IR 8xx Platform Architecture
Virtual Machine
  PaaS
  App
Virtual Machine
  IOx
Virtual Machine
  IOS
Hypervisor
IR829/809 Hardware

## Slide 6: Conceptual Design
Wifi User
IR829
Car Controller
Ride-on
Serial
rtsp
Virtual Machine
  PaaS
  App
Virtual Machine
  IOx
Virtual Machine
  IOS
Hypervisor
hardwired
http
IP Cam

## Slide 7: Car Control PaaS App
Python HTTP Server
  HTML5 App
  Authenticate users
  Grab Session ID from IP Camera
Websocket
  Javascript maps keyboard and buttons clicks into car instructions
Serial Worker Threads
  Receive commands from web socket
  Issue/read commands over over serial

## Slide 8: Car Control PaaS App
Packaged for deployment
Deployed on Router
Resources
Mapped Serial Interface
App Info

## Slide 9: PaaS App Configuration File
Provides flexibility to change settings once the app is deployed
  Server port and authentication settings
  IP Cam connection details
  Serial Baud
  Debug/Other logging to troubleshoot app

## Slide 10: The Electronics
Relays
Power Supply
RS232
to TTL
Arduino

## Slide 11: Arduino Microcontroller
Arduino Microcontroller is used to
  Switch relays
  Provide serial to hardware interface
Firmware
  Continually read serial buffer
  Detect F,B, L or R commands
  Switch correct relay for 500ms

## Slide 12: Considerations
This is a simple use example of what can be achieved simply and fairly quickly
The Car is now IP enabled, can control from anywhere world wide as long as there is IP connectivity
Security considerations should be top of mind in development of IOx systems

## Slide 13: Questions?